Selection API & Non-STD/DV_TIMINGS Devices

---
Selection API & Non-STD/DV_TIMINGS Devices
Devices without S_STD or S_DV_TIMINGS support cannot scale/compose outside the width/height as set by S_FMT unless the hardware resolution is fixed or scaling and cropping is not allowed.

---
Proposal
- Add a G/S_FRAMESIZE ioctl.
- Add new input capabilities:
  - V4L2_IN_CAP_FRAMESIZE: supports G/S_FRAMESIZE.
  - V4L2_IN_CAP_FIXED: has a single fixed frame size. Equivalent to CAP_FRAMESIZE with one fixed frame size.
  - V4L2_IN_CAP_COMPOSE_SIZE: frame size == compose size. No scaling, no cropping.
- Ditto for the output capabilities, except for:
  - V4L2_OUT_CAP_CROP_SIZE: frame size == crop size. No scaling, no composing.
- Affects: vivi, m2m and sn9c102 (probably incorrectly implements ENUM_FRAMESIZES).

---
Proposal
- Extend vivi with IN_CAP_FRAMESIZE or IN_CAP_COMPOSE_SIZE?
- General problem: adding IN_CAP_FRAMESIZE to an existing driver changes the driver behavior. S_FMT will now scale instead of setting the frame size. Example: UVC, vivi.

---
S_FRAMESIZE & M2M
- Currently S_FMT + crop defines the rectangle towards the device and S_FMT + compose defines the rectangle from the device.
- Equivalent to V4L2_IN_CAP_COMPOSE_SIZE and V4L2_OUT_CAP_CROP_SIZE.
- If a M2M device allows composing/scaling for output buffers or cropping/scaling for capture buffers, then S_FRAMESIZE must be implemented.
- Are there any devices like that?

---
Selection API & S_FMT Order
- Currently the ordering is as follows:
  - S_STD/S_DV_TIMINGS/S_FRAMESIZE resets crop/compose/fmt.
  - S_FMT/Crop/Compose: order dependent, i.e. the driver should give priority to the requested rectangle, changing others to match.
  - Exception: TRY_FMT which keeps existing crop/compose rectangles unchanged.
- Is there any need to change this?
- Recommendation:
  - for capture: crop (sets compose/fmt rectangles), compose (sets fmt rectangle), s_fmt (only changes fmt rectangle iff fmt contains compose rectangle).
  - for output: compose (sets crop/fmt rectangles), crop (sets fmt rectangle), s_fmt (only changes fmt rectangle iff fmt contains crop rectangle).

---
TRY_FMT and -EINVAL
- VIDIOC_TRY_FMT shouldn't return -EINVAL when an unsupported pixelformat is provided
  - In practice video capture board do.
  - Webcam drivers don't.
  - Some applications rely on the -EINVAL error code.
- Proposal 1: leave it as driver-dependent behavior, but specify that an unsupported pixelformat is the only reason why TRY_FMT might return -EINVAL.
- Proposal 2: be more specific: -EINVAL should be returned for video capture devices (i.e. devices supporting S_STD or S_DV_TIMINGS) and 0 for all others. But I am unsure what more m2m devices do.

---
V4L2 Support Libraries
- Existing libs:
  - libv4l1/libv4l2/libv4lconvert: format conversions, V4L1 -> V4L2 translation, plugins.
  - libv4l2rds: RDS decoding. Still missing: translate TMC data to readable text.
- Potential libs:
  - libv4l2raw2sliced: raw VBI decoding (currently part of qv4l2).
  - libv4l2alsa: alsa streaming (currently part of qv4l2 and xawtv).
  - Analog TV frequency tables, currently in libv4l2util. Also contains v4l2_driver.c (v4l2 wrapper, undocumented, IMHO a bad design).

---
V4L2 Support Libraries
- libmediactl library: in external git repo. Move to v4l-utils?
- libmedia_dev: search for associated nodes. Still waiting for replacement, what's the status?
- Support library documentation?

---
Colorspaces
- No known colorspace: V4L2_COLORSPACE_UNKNOWN.
  Decided to add this during the Barcelona summit last year, still not done, though.
- Limited Range RGB. Same as sRGB, but the data is in the range 16-235 instead of 0-255. Proposal: V4L2_COLORSPACE_SRGB_LIM.
- Setting colorspace for output devices, spec says: “This information supplements the pixelformat and must be set by the driver”. For output devices this has to be set by userspace. Change the spec accordingly? Already done like that by m2m devices.